## Slide 1: stability by Routh-Hurwitz Criterion
Nafees Ahamad
AP, Department of Electrical, Electronics & Communication, DIT University, Dehradun

## Slide 2: Contents
Stability
Why investigate stability ?
Example of unstable system
Routh-Hurwitz Criterion
Rules
Special Cases
Practical Use
References

## Slide 3: Stability
A system is stable if every bounded input results in bounded output.
A system is unstable if any bounded input results in unbounded output.

## Slide 4: Why investigate stability ?
Most important consideration in design a control system.
An unstable system is of NO use practically.

## Slide 5: Example of unstable system
Collapse of Tacoma Narrows Bridge (US state of Washington ) in 1940.
It opened to traffic on July 1, 1940, and dramatically collapsed into Puget Sound on November 7 the same year.
Source: Wikipedia

## Slide 6: Stability
Consider following closed loop system
Its closed loop transfer function
Its characteristic equation

## Slide 7: Stability…
Roots of characteristic equation (=poles of transfer function)
,
All roots are on right hand side of s-plane.
So, system is unstable.
,
Re
Im

## Slide 8: Stability…
If any root lies on LHS of s-plane, then system becomes stable.
If simple root(s) is on imaginary axis then system becomes marginally stable.
If multiple roots are on imaginary axis then system becomes marginally unstable.

## Slide 9: Stability – Practically
Stable system: If the natural response becomes zeros as time approaches infinity.
Unstable system: if the natural response grows without bound as time approaches infinity.
Marginally stable system : if the natural response neither decays nor grows but remains constant or oscillates as time approaches infinity.

## Slide 10: Roots and Response

## Slide 11: Roots and Response …

## Slide 12: Routh-Hurwitz Criterion
By Routh-Hurwitz Criterion we can find out number of roots with +ve, -ve and zero real parts.
That is we can find out the stability of a system.

## Slide 13: Routh-Hurwitz Criterion
Consider a system with characteristic equation
…
Necessary condition
  All the coefficients of the characteristic equ should have same sign.
  There should not be any missing term.
If above two conditions are not satisfied then system will be unstable.
If above two conditions are satisfied then It is not guaranteed that system is stable for that we need to apply Routh-Hurwitz Criterion.

## Slide 14: Routh-Hurwitz Criterion…
sn | a0 | a2 | a4
Sn-1 | a1 | a3 | a5
Sn-2 | b1 | b2 | 
Sn-3 | c1 |  | 
- | - | - | 
- | - | - | 
s0 | - |  | 
If no sign change in first column All roots are on LHS of s-plane Stable system

## Slide 15: Example
Example 1: Check the stability of the system whose characteristic equation is given by
Necessary conditions are satisfied
  All the coefficients of the characteristic equation have same sign
  There is no missing term
Make Routh array

## Slide 16: Example …
s4 | 1 | 6 | 1
s3 | 2 | 4 | 0
s2 | 4 | 1 | 
s1 | 3.5 |  | 
s0 | 1 |  | 
No sign change in first column All roots are on LHS of s-plane Stable system

## Slide 17: Example…
Example 2: Check the stability of the system whose characteristic equation is given by
Necessary conditions are satisfied
  All the coefficients of the characteristic equation have same sign
  There is no missing term
Make Routh array

## Slide 18: Example …
s4 | 2 | 1 | 2
s3 | 2 | 3 | 0
s2 | -2 | 2 | 
s1 | 5 |  | 
s0 | 2 |  | 
Two sign change in first column Two roots are on LHS of s-plane Unstable system

## Slide 19: Example: Special case 1 ( First element in a row of Routh array is zero)
Example 3: Check the stability of the system whose characteristic equation is given by
Necessary conditions are satisfied
  All the coefficients of the characteristic equation have same sign
  There is no missing term
Make Routh array

## Slide 20: Example: Special case 1 …
s5 | 1 | 2 | 3
s4 | 1 | 2 | 5
S3 | 0 | -2 | 
s2 |  |  | 
s1 |  |  | 
s0 |  |  | 
This is the special case where first element of a row is zero.
Replace zero with a very small +ve number say and continue the procedure.
Finally put and note the number of sign changes

## Slide 21: Example: Special case 1 …
s5 | 1 | 2 | 3
s4 | 1 | 2 | 5
S3 |  | -2 | 
s2 |  | 5 | 
s1 |  | 0 | 
s0 | 5 |  | 
s5 | 1 | 2 | 3
s4 | 1 | 2 | 5
S3 |  | -2 | 
s2 |  | 5 | 
s1 |  | 0 | 
s0 | 5 |  | 
Two sign change in first column Two roots are on RHS of s-plane Unstable system
Note: Alternate method
Multiply characteristic equ with (s+a). Where ‘a’ is any +ve real number.
The simplest value of ‘a’ is 1. So, multiply cha equ with (s+1) and apply normal procedure.

## Slide 22: Example: Special case 2 ( Any one row of Routh array is zero)
Example 4: Check the stability and position of roots of the system whose characteristic equation is given by
Necessary conditions are satisfied
  All the coefficients of the characteristic equation have same sign
  There is no missing term
Make Routh array

## Slide 23: Example: Special case 2 …
s6 | 1 | 8 | 20 | 16
s5 | 2 | 12 | 16 | 
s4 |  |  |  | 
S3 |  |  |  | 
s2 |  |  |  | 
s1 |  |  |  | 
s0 |  |  |  | 
Note: We can also divide any row by a common factor
Divide each by 2

## Slide 24: Example: Special case 2 …
s6 | 1 | 8 | 20 | 16
s5 | 1 | 6 | 8 | 
s4 | 1 | 6 | 8 | 
S3 | 0 | 0 |  | 
s2 |  |  |  | 
s1 |  |  |  | 
s0 |  |  |  | 
Vanishing row
Auxiliary row
A(s)=1s4+6s2+8

## Slide 25: Example: Special case 2 …
Auxiliary equation
A(s)=1s4+6s2+8
Take the first derivative of above equation
Put the coefficients of in vanishing row and proceed

## Slide 26: Example: Special case 2 …
s6 | 1 | 8 | 20 | 16
s5 | 1 | 6 | 8 | 
s4 | 1 | 6 | 8 | 
S3 | 4 | 12 |  | 
s2 |  |  |  | 
s1 |  |  |  | 
s0 |  |  |  | 
Divide each by 4

## Slide 27: Example: Special case 2 …
s6 | 1 | 8 | 20 | 16
s5 | 1 | 6 | 8 | 
s4 | 1 | 6 | 8 | 
s3 | 1 | 3 |  | 
s2 | 3 | 8 |  | 
s1 | 1/3 |  |  | 
s0 | 8 |  |  | 
No sign change in first column No roots on RHS of s-plane. Now system may be marginally stable.

## Slide 28: Example: Special case 2 …
Now, system may be marginally stable.
Find out the roots of auxiliary equation A(s)=1s4+6s2+8 = 0
Put s2 = x in above equ.
These two pairs of the roots are also the roots of the original characteristic equation.
So, 4 roots are on Imaginary axis, 2 roots are on LHS of s-plane.
Hence, system is marginally stable.

## Slide 29: Application of Routh – Hurwitz criterion
Example 5: The open loop transfer function of a feedback control system is given by
Find the range of the values of K for stability, also determine the stability of the system when K = 12.
Answer: 0<K<11.56 and at K = 12 system is Unstable.

## Slide 30: Thanks ?