## Slide 1: Nyquist Stability Criterion
By: Nafees Ahamad
AP, Department of EECE, DIT University,
Dehradun

## Slide 2: Introduction
Nyquist stability criterion is based on the principle of argument.
The principle of argument is related with the theory of mapping.

## Slide 3: Mapping
Consider a function D(s) = s2 + 1
Let s1 = 2+4j
So, D(s1) = (2+4j)2+1 = -11+j16 = u+jv
Therefore any point s1 in s-plane can be mapped in D(s) plane by locating the values of ‘u’ and ‘v’.

## Slide 4
Im
Re
S-plane
s1= 2+j4
2
4
Im
Re
D(s)-plane
-11
16
D(s1)= -11+j16
Mapped

## Slide 5: Mapping…
Therefore, every point in s-plane maps into one and only one point in D(s) plane.
Any closed contour in s-plane maps into the closed contour in D(s) plane.

## Slide 6: Mapping of closed contour and principle of argument
Consider the characteristic equation
Where are zeros and are poles.
Let then D(s) will also be complex .
Now a arbitrary closed ‘C’ in s-plane maps onto the D(s) plane as contour as shown on next slide

## Slide 7
Im
Re
S-plane
Im
Re
D(s)-plane
Mapped
C
No Poles & Zeros inside the contour ‘C’

## Slide 8: Mapping of closed contour and principle of argument…
Consider this contour ‘C’ in s-plane.
This contour encircles neither zeros nor poles, then the contour ‘’ in D(s) plane can’t encircle the origin or the point at infinity.
If we trace the contour ‘C’ in clockwise direction then the inside region will be on right of the contour.
The corresponding region in D(s) plane which contains neither origin nor the point at infinity should also be to the right of the contour

## Slide 9: Mapping of closed contour and principle of argument…
If the contour ‘C’ encircles zero but not poles then the point D1(s) is given by
Where
IT means that the trip of forms a close contour about the origin in clockwise direction as shown on next slide.

## Slide 10
Im
Re
S-plane
Im
Re
D(s)-plane
Mapped
C
Zeros
One Zero inside the contour ‘C’

## Slide 11: Mapping of closed contour and principle of argument…
From previous slide we can say that the tip of forms a closed counter about the origin in clockwise direction.
Similarly, if the contour ‘C’ encircles ‘z’ zeros in clockwise direction then the contour in D(s) plane encircles the origin of D(s) plane ‘z’ times in clockwise direction.
This is shown on next slide for z = 2.

## Slide 12
Im
Re
S-plane
Im
Re
D(s)-plane
Mapped
C
Two Zero inside the contour ‘C’

## Slide 13: Mapping of closed contour and principle of argument…
Consider another case when the contour ‘C’ encircles ‘P’ number of poles in clockwise direction then the corresponding contour ‘’ will encircle the origin ‘P’ time in anti-clockwise direction.
Next two slides show this situation when P =1 and P = 2.

## Slide 14
Im
Re
S-plane
Im
Re
D(s)-plane
Mapped
C
One pole inside the contour ‘C’

## Slide 15
Im
Re
S-plane
Im
Re
D(s)-plane
Mapped
C
Two poles inside the contour ‘C’

## Slide 16: Mapping of closed contour and principle of argument…
Now, if contour ‘C’ encircles both zeros and poles in clockwise direction then corresponding contour ‘’ encircles the origin of D(s) plane N (=Z-P) time in clockwise direction.
This relationship between enclosure of poles and zeros by the contour in s-plane and encirclement of origin of the contour ‘’ in D(s) plane is known as principle of argument.

## Slide 17: Nyquist path or Nyquist Contour
The overall transfer function of a given system is given by
, Its characteristic equation
For stability of closed loop system this characteristic equation should not have any root (Pole of T.F) on right half of s-plane.
For this purpose, we use a contour in s-plane which enclosed the entire right half of s-plane with clockwise encirclement and radios .
This contour is know as Nyquist Contour. (See on next slide)

## Slide 18: Nyquist path or Nyquist Contour …
No Poles on axis
One Poles at origin
Poles at origin and axis

## Slide 19: Nyquist Criterion
The characteristic equation is given by
Let there are ‘Z’ zeros and ‘P’ poles of D(s) in the right hand side of s-plane.
If this contour is mapped in D(s) plane as then encloses the origin N times (N = Z – P) in clockwise direction.
Then the system becomes unstable because the clockwise encirclement is possible only when there are zeros of D(s) in right half of s-plane

## Slide 20: Nyquist Criterion …
A feedback system (closed loop system) is stable if and only if there is no zeros of D(s) in the right half of s-plane. i.e., Z = 0
N = Z – P = - P
Therefore, for a closed loop system to be stable, the number of counter clockwise encirclement of the origin of D(s) plane by should equal the number of right half s-plane poles of D(s) [which are the poles of open loop transfer function G(s)H(s)].

## Slide 21: Nyquist Criterion …
Since
Or
The contour in D(s) plane can be mapped in G(s)H(s) plane by shifting horizontally to the left by one unit.
Contour
Contour
Im
Re
-1

## Slide 22: Nyquist Criterion …
Thus the encirclement of the origin by the contour is equivalent to the encirclement of the point (-1+j0) by the contour as shown on previous slide.
In most, single loop feedback system G(s)H(s) has no poles in the right half plane i.e. P = 0 then close loop system is stable if N = P = 0.
So, we can say that a closed loop system with P = 0 is stable if the net encirclement of the origin of D(s) plane by contour is zero.

## Slide 23: Nyquist Stability Criterion: Statement
A feedback system is stable if the contour of the open loop transfer function G(s)H(s) corresponding to the Nyquist contour in the s-plane encircles the point (-1+j0) in counter clockwise direction and the number of counter clockwise encirclement about the (-1+j0) equals the number of poles of G(s)H(s) in the right half of the s-plane i.e. with positive real parts.
In common case, the closed loop system is stable if the contour of G(s)H(s) does not pass through or does not encircle (-1+j0) point, i.e. net encirclement is zero

## Slide 24: Example
Consider the following example
Draw the polar plot:
Put ω=+0
    Assuming 1>>j0T
Put ω=+∞
    Assuming 1<<j ∞ T
Separate the real & Im parts
  So, No intersection with jω axis other then at origin and infinity

## Slide 25: Example …
Polar plot ⇒ω=+0 to ω=+∞
Plot for variation from ω=-0 to ω=-∞ is mirror image of the plot from ω=+0 to ω=+∞. As shown by doted line.
From ω=-0 to ω=+0 the plot is not complete. The completion of plot depends on the no of poles of G(s)H(s) at origin(Type of the G(s)H(s)).
Im
Re
Nyquist Plot

## Slide 26: Closing Nyquist plot from s=-j0 to s=+j0…
The closing angle for different type of sys
Type of G(s)H(s) (n) | Angle through which Nyquist plot is to be closed from ω=-0 to ω=+0 | Magnitude of G(s)H(s)
0 | 0 | The points ω=-0 & ω=+0 are coincident
1 | -π | ∞
2 | -2π | ∞
3 | -3π | ∞
. |  | 
. |  | 
n | -nπ | ∞

## Slide 27: Example…
Im
Re
Nyquist Plot

## Slide 28: Example…
No of roots of characteristic equation having + real part(Z) are given by
  N=0 As point -1+j0 is not encircled by the plot
  P=0 (Poles of G(s)H(s) having + real parts)
  No of roots of characteristic equation (Z) with +ve real part = 0
Hence, closed loop system is stable

## Slide 29
Thanks