DC Motor Design

(© Dr. R. C. Goel & Nafees Ahmed )

By

Nafees Ahmed

Asstt. Prof. Department of Electrical Engineering

DIT, University, Dehradun, Uttarakhand

References:

- Notes by Dr. R. C. Goel

- Electrical Machine Design by A.K. Sawhney

- Principles of Electrical Machine Design by R.K Agarwal

- VTU e-Learning

- www.google.com

- www.wikipedia.org

DC Machine Design

Output Equation: -

It gives the relationship between electrical rating and physical dimensions (Quantities)

Output of a DC machine

Where

Eg  = Generated voltage

= Flux per pole

P = No of poles

N = Speed in RPM

Z = Total no of armature conductors

Ia= Armature current

IZ = Current per conductor

Total Ampere conductors is known as total electric loading

Specific electric loading

It is defined as electric loading per meter of periphery, denoted by .

Or

So put the above values equation (1) can be written as

Where

D = Inner diameter of stator

L = Length of the IM

= 0.45 to 0.75 T

= 15000 to 20000 	ac/m	for 4-20 	Kw

= 25000 to 31000 	ac/m	for 50-200 	Kw

= 36000 to 50000 	ac/m	for >500  	Kw

Design procedure of DC machin:

- Estimation of main dimensions (D, L)

We know

Where

Solving equation (1) & (2) we can find out D & L.

- Check for D & L

Peripheral speed

- Length of air gap

- Find effective length

Ventilating ducts are required when L>12 Cm and for every 7 to 8 Cm, we provide 0.8 cm ventilating duct.

Generally

l1= l2= l3=……….= ln

Let

nv =No of ventilating ducts

bv = Width of one ventilating duct

Gross Iron length

l = l1+ l2+ l3+………. +ln

Actual Iron length

li    =Ki*l

Where 	Ki =Stacking factor

=0.90 to 0.92

Overall length

L = l+nv*bv

Effective length

Where	 =Effective width of ventilating duct (< bv due to fringing)

- Design of winding

Armature slots

No of conductors per slot

Must be an integer and divisible by 2 for double layer windings. If not an integer make it integer and hence find the corrected value of  that is. Also find out the corrected values of followings

Armature current

X-sectional area of conductor

- Design of commutator

No of commutator segments

C= No of coils

No of conductors in parallel path

No of turns

Width of each commutator segments

=3 to 4 mm

Mica insulation

=0.8 mm

Dia of commutator

DC= (0.6 to 0.8) D

The voltage per commutator segment should be between 25 to 30 volts.

- Find Characteristics

Find out core loss and Cu loss and efficiency

# Text boxes

bv

l1

l2

l3

ln

L