Assignment:-2

Note: - All resistances are in ohm (Ω)

Q1.	Derive expressions for Average Value, RMS Value, Peak Factor & Form Factor for the following wave

Q2.	Three Sinusoidal Voltages acting in series are given by

V1=10 sin 440t, V2=10√2 sin (440t-450), V3=20 cos 440t

Determine:-

- An expression fro the resultant voltage

- The frequency & rms value of the resultant voltage

Q3.	Do as directed

- Show that the instantaneous power consumed in a pure resistive circuit is not constant but it is fluctuating.

- Show that the Average power consumed by pure L & C is zero.

Q4.	Explain the terms

(i) Apparent Power (ii) Active Power (iii) Reactive Power (iv) Power Factor

Q5.	Determine (Fig. 2)

- The current & power consumed in each branch.

- The supply current & power factor.

Q6.	Total power consumed by both branches of the circuit shown in Fig. 3 is 2200 W. Calculate the power of each breach and the reading of the ammeter.

Q7.	Two impedances given by Z1= (10+j15) Ω & Z2= (6-j8) Ω are connected in parallel. If the total current supplied is 15 A, calculate the current & power absorbed by each branch.

Q8.	In the series parallel circuit of Fig. 4 the parallel branches A & B are in series with C. The impedance are ZA= (4+j3) Ω, ZB= (10-j7) Ω & ZC= (6+j5) Ω. If the voltage applied to the circuit is 200 V at 50 Hz, calculate

- Current IA, IB & IC.

- The total power factor for the whole

circuit. Draw vector diagram also.

Q9.	In the following circuit (Fig. 5), the reactance of

the capacitor C1 is 4 Ω, the reactance of  C2 is 8 Ω

and  the reactance of L is 8 Ω. A sinusoidal

voltage of 120 V is applied to the circuit.

Find (i) current in each branch

(ii) power loss in the circuit.

Q10.	In the circuit (Fig.6), determine the

voltage at 50 Hz to be applied across AB

in order that a current of 10 A flows in the

capacitor.

Q11.	State& explain the condition of series & parallel resonance. Why series & parallel resonance are also called voltage & current resonance respectively? Also explain what acceptor & rejecter circuits are.

Q12.	 A series circuit consists of a resistance of 4 Ω, an inductance of 0.5 H & a variable capacitance in series across a 100 V, 50 Hz supply.

Calculate

(i) 	The value of capacitance to produce resonance,

- Voltage across the capacitance, &

(iii) 	Q-factor of the circuit.

Q13.	Determine the frequency at which the

voltage Vo is zero in Fig 7.

Q14.	In the circuit (Fig. 8), find the value of R such

that the impedance of the whole circuit should

be independent of the frequency of the supply.

If voltage = 200 V, L = 0.16 H & C = 100 µF,

calculate the power loss in the circuit.

- Three identical coils connected in delta across 400 V, 50 Hz, 3- phase ac supply, take a line current of 17.32 A at power factor of 0.8 lagging. Calculate (i) The phase current (ii) the resistance and inductance of each coil (iii) the power drawn by each coil. (Ans: IP=10 A, RP=32, L=76.4 mH, P= 3200 Watt)

- If the phase voltage of a 3-phase star-connected system is 200 V, what will be the line voltages?

a.	 When the phases are correctly connected

b.	 When connections to one of the phases are reversed? (Ans: (a) EL=346.11 V each (b) 200 V,200 V, 346.41 V)

- Three 50 Ω resistances are connected in star across 400 V, 3 -  supply. Find (i) phase current, line current and power taken from the mains. (ii) What would be the above values if one of the resistors were disconnected? (Ans.:- (i) 4.62 A, 4.62 A, 1600 W, (ii) 4 A, 4 A, 3200 W)

- With the aid of a phasor diagram show that the power and power factor of a balanced 3-phase load can be measured by two wattmeters.

- For a certain load, one of the wattmeter reads 20 kW and the other 5 kW. Calculate the power and power factor of the load when (i) both wattmeters read positive value (ii) one wattmeter reads negative value. (Ans.:-25 KW, 0.6933, 15 KW, 0.3273).

- Three equal impedances, each consisting of R and L in series are connected in star and are supplied from a 400 V, 50 Hz, 3 – phase, 3 – wire balanced supply system. The power input to the load is measured by 2 – wattmeter method and the two wattmeters read 3 kW and 1 kW. Determine the values of R and L connected in each phase. (Ans.:- 22.856 Ω, 63 mH)

- A 3-phase 500 V motor has 0.4 power factor lagging. Two wattmeters are connected to measure the input, they show the total input to be 30 kW. Find the reading of each wattmeter. (Ans: - 34.843 & -4.843 Watts)

# Text boxes

Ans:-

Vav=Vm/Pi , Vrms=Vm/2 ,

Kp=2, Kf=1.57

Vm

1800

3600

5400

7200

Fig.1

Ans:-

V=22.36 sin(440t+26.560)

f =70 Hz, Vrms=15.81 V

Ans:-

I1=10   450 I2=10   -150  I3=10   1050

1000 W, 500 W, 500 W,

I=20   450 , P.F.=1.0

Ans:-

P1=1200 W, P2=1000 W, I=19.23 A

Ans:-

I1=(1.967-j8.361) A, I2=(13.033+j8.361) A,

P1=738 W, P2=1438 W,

Ans:-

IA=14.2  -51.250 A, IB =5.82  20.650   A,

I C=16.95  -32.20   A, P.F = 0.846 lagging

Ans:- Iab=(4.8+j3.6) A, Ibc=(-2.4+j13.2) A,

IL=(7.2-j9.6) A, Power = 576 W,

Ans:-  (267.33-j108.8) volts

Ans:-  C = 20.264 µF, V = 3927 V, Q-factor = 39.27

Ans:-  fr = 2250 Hz

Ans: - R =40 Ω, P = 1 KW