Assignment:-3

(Measuring Instruments & 3-Phase AC circuits)

- Explain construction and working principle of attraction type & repulsion type moving iron instruments.

- Explain construction and working principle of PMMC & dynamometer type moving coil instruments.

- A moving coil instrument gives a full scale deflection of 10 mA and pd across its terminals is 100 mV. Calculate

  - Shunt resistance for full scale deflection corresponding to 200 A. (To work as an ammeter)

  - Series resistance for full scale reading corresponding to 1000 V. (To work as a voltmeter)

(Ans: - (a) 5.00025 * 10-4 ohm, (b) 99990 ohm)

- Three identical coils connected in delta across 400 V, 50 Hz, 3- phase ac supply, take a line current of 17.32 A at power factor of 0.8 lagging. Calculate (i) The phase current (ii) the resistance and inductance of each coil (iii) the power drawn by each coil. (Ans: IP=10 A, RP=32, L=76.4 mH, P= 3200 Watt)

- If the phase voltage of a 3-phase star-connected system is 200 V, what will be the line voltages?

a.	 When the phases are correctly connected

b.	 When connections to one of the phases are reversed? (Ans: (a) EL=346.11 V each (b) 200 V,200 V, 346.41 V)

- Three 50 Ω resistances are connected in star across 400 V, 3 -  supply. Find (i) phase current, line current and power taken from the mains. (ii) What would be the above values if one of the resistors were disconnected? (Ans.:- (i) 4.62 A, 4.62 A, 1600 W, (ii) 4 A, 4 A, 3200 W)

- With the aid of a phasor diagram show that the power and power factor of a balanced 3-phase load can be measured by two wattmeters.

- For a certain load, one of the wattmeter reads 20 kW and the other 5 kW. Calculate the power and power factor of the load when (i) both wattmeters read positive value (ii) one wattmeter reads negative value. (Ans.:-25 KW, 0.6933, 15 KW, 0.3273).

- Three equal impedances, each consisting of R and L in series are connected in star and are supplied from a 400 V, 50 Hz, 3 – phase, 3 – wire balanced supply system. The power input to the load is measured by 2 – wattmeter method and the two wattmeters read 3 kW and 1 kW. Determine the values of R and L connected in each phase. (Ans.:- 22.856 Ω, 63 mH)

- A 3-phase 500 V motor has 0.4 power factor lagging. Two wattmeters are connected to measure the input, they show the total input to be 30 kW. Find the reading of each wattmeter. (Ans: - 34.843 & -4.843 Watts)