- Explain construction and working principle of a 3-phase indcuiton motor.

- Explain the terms slip, slip frequency, wound rotor and cage rotor.

- Draw and explain the torque-slip & torque-speed charactoristics of a typical 3-phase induction motor. Mark the starting torque and maximum troque on the daigram so drawn.

- Explain  the terms air-fap power Pg, inernal mechanical power developed and shaft power Psh. How  are these terms related with each others. Hence show that :

Pg :Rotor ohmic loss : Pm =1 :s (1-s)

- A 3-phase induction motor runs at 1140 rpm at full load when supplied with power from a 60 Hz, 3-phase line calculate

(i)	No of poles.

(ii)	Slip at full load.

- Frequency of rotor voltage.

- Speed of rotor field with respect to rotor.

- Speed of rotor field with respect to stator and stator field.

- Speed of rotor at a slip of 10% and rotor frequency at this speed.

- If the applied voltage per phase is 230 V, find th0 rotor induced emf at stand still and at 10% slip, with stator to rotor turn ration of 1: 0.5

(Ans: - (i) 1200 rpm, (ii) 5% (iii) 3 Hz (iv) 60 rpm (v) 0 rpm (vi) 1080 rpm, (vii) 11.5 V)

- A 6-pole, 3-phase indcution motor develops 30 hp including 2 hp mechanical losses at a speed of 950 rpm on 550 V, 50 Hz mains. The power factor is 0.88 lagging. Calculate (i) slip (ii) rotor copper loss (iii) total input if stator losses are 2 kW (iv) efficiecny (v) line current. (Ans : - (i) 0.05, (ii) 1161 Watts, (iii) 20594 Watts, (iv) 81.64% (v) 30 A)

- Explain construction and principle of operation of 1-phase induction motor.

- Why single phase induciton moto is not self starting ?

- What are the different methods of statring a single phase induction motors and what are the diffenet types of 1-phase induction motors ?