- Obtain expression for output equation of a rotating machine. Apply this for a synchronous, induction and dc machine.

- Discuss factors affecting size of rotating machine and how the separation of main dimensions is done.

- Explain SCR in synchronous machines.

- Find the main dimensions of a 20 MVA, 11kV, 50Hz, 150r.p.m., 3-phase water wheel generator. The average gap density is 0.6 Wb /m² and ampere conductors per meter are 35,000. The peripheral speed should not exceed 65 m/s at normal running speed in order to limit the run-away speed.

- Give procedure for designing the field system of a three-phase turbo generator from the given design data. Also indicate how much excitation power may be required for such a generator of about 100 MW capacity.

- A 1500 kVA, 3-phase, star-connected, 3300 V, 250 rpm water wheel generator has the following design data:

Effective gap length			= 7mm

Effective gap area/pole		= 0.075 m²

Winding factor 			= 0.955

Field mmf per pole under  rated condition		= 7850 A

No. of field turns/pole			= 180

The peak value of fundamental flux density distribution B…= 0.94 T and peak value of the actual flux density distribution B…=0.9T.

The permissible value of current density in field winding is 3 A/mm². Determine:

- Turns  / phase

- MMF for air gap

- Armature MMF /pole

- Field current

- Sectional area of field conductor.

- Design the suitable values of diameter and length of a 75 MVA, 11 KV, 50 Hz, 3000 rpm, 3-phase star connected alternator. Also determine the value of flux, conductor per slot, no of turns per phase, and size of armature conductor. Given

Average gap density		= 0.6	T

Amp conductor per m		= 50,000

Peripheral speed 		= 180 m/s

Current density		= 6 A/m2

- Calculate the diameter, core length, number of conductors of the stator, size of conductor, number of stator slots of a 30 MVA, 11KV, 3000 r.p.m. 50Hz star connected turbo alternator. Assume suitable data:

Bav =0.55 Wb/m², 	ac =55000 A/m, 	Kw = 0.955,

Peripheral velocity = 160 m/s.

- If two synchronous machines running at the same speed and having the same number of poles, the physical dimensions are in the ratio 3 : 2. Compare the outputs, armature copper losses and iron losses in the two machines. Assume specific magnetic loading and current density to be same for both the machines.