## Slide 1: Bode Plot
Nafees Ahmed
Asstt. Professor, EECE Deptt
DIT University, DehraDun

## Slide 2
Poles & Zeros and Transfer Functions
Transfer Function:
A transfer function is defined as the ratio of the Laplace
transform of the output to the input with all initial
conditions equal to zero. Transfer functions are defined
only for linear time invariant systems.
Considerations:
Transfer functions can usually be expressed as the ratio
of two polynomials in the complex variable, s.
Factorization:
A transfer function can be factored into the following form.
The roots of the numerator polynomial are called zeros.
The roots of the denominator polynomial are called poles.

## Slide 3: Poles, Zeros and S-Plane
An Example:
You are given the following transfer function. Show the
poles and zeros in the s-plane.
S - plane
x
x
o
x
o
0
-4
-8
-10
-14
origin
 axis
j
axis

## Slide 4: Bode Plot
It is graphical representation of transfer function to find out the stability of control system.
It consists of two plots
  Magnitude (in dB) Vs frequency plot
  Phase angle Vs frequency plot

## Slide 5: Bode Plot…
Consider following T.F
Put s=jw
Arrange in following form

## Slide 6: Bode Plot…
So
Hence Bode Plot consists of two plots
  Magnitude ( dB) Vs frequency plot (w)
  Phase angle ( )Vs frequency plot (w)
Magnitude
Phase Angle

## Slide 7: Bode Plot…
Magnitude in dB
Phase Angle

## Slide 8: Bode Plot…
Type of System | Initial Slope | Intersection with 0 dB line
0 | 0 dB/dec | Parallel to 0 axis
1 | -20dB/dec | =K
2 | -40dB/dec | =K1/2
3 | -60dB/dec | =K1/3
. | . | .
. | . | .
. | . | .
N | -20NdB/dec | =K1/N

## Slide 9: Bode Plot Procedure
Steps to draw Bode Plot
  Convert the TF in following standard form & put s=jw
  Find out corner frequencies by using

## Slide 10: Bode Plot Procedure …
  Draw the magnitude plot. The slope will change at each corner frequency by +20dB/dec for zero and -20dB/dec for pole.
    For complex conjugate zero and pole the slope will change by
  Starting plot
    For type Zero (N=0) system, draw a line up to first (lowest) corner frequency having 0dB/dec slope of magnitude (height) 20log10K
    For type One (N=1) system, draw a line having slope
    -20dB/dec from w=K and mark first (lowest) corner frequency.
    For type One (N=2) system, draw a line having slope
    -40dB/dec from w=K1/2 and mark first (lowest) corner frequency.

## Slide 11: Bode Plot Procedure …
Draw a line up to second corner frequency by adding the slope of next pole or zero to the previous slope and so on….
  Slope due to a zero = +20dB/dec
  Slope due to a pole = -20dB/dec
Calculate phase angle for different value of ‘w’ and draw phase angle Vs frequency curve

## Slide 12: Bode Plot GM & PM
Gain Margin: It is the amount of gain in db that can be added to the system before the system become unstable
  GM in dB = 20log10(1/|G(jw|) = -20log10|G(jw|
  Gain cross-over frequency: Frequency where magnitude plot intersect the 0dB line (x-axis) denoted by wg
Phase Margin: It is the amount of phase lag in degree that can be added to the system before the system become unstable
  PM in degree = 1800+angle[G(jw)]
  Phase cross-over frequency: Frequency where phase plot intersect the 1800 dB line (x-axis) denoted by wp
  Less PM => More oscillating system

## Slide 13: Bode Plot GM & PM

## Slide 14: Bode Plot & Stability
  Stable
    If wg<wp => GM & PM are +ve
  Unstable
    If wg>wp => GM & PM are –ve
  Marginally stable
    If wg=wp => GM & PM are zero

## Slide 15: Bode Plot Examples
Example 1:Sketech the Bode plot for the TF
Determine
(i) GM
(ii) PM
(iii) Stability

## Slide 16: Bode Plot Examples…
Solution:
  Convert the TF in following standard form & put s=jw
  Find out corner frequencies
    So corner frequencies are 10, 1000 rad/sec

## Slide 17: Bode Plot Examples…
How to draw different slopes

## Slide 18: Bode Plot Examples…
Magnitude Plot

## Slide 19: Bode Plot Examples…
Phase Plot
S.No | W | Angle (G(jw)
1 | 1 | ----
2 | 100 | -900
3 | 200 | -980
4 | 1000 | -134.420
5 | 2000 | -153.150
6 | 3000 | -161.360
7 | 5000 | -168.570
8 | 8000 | -172.790
9 | Infi | -1800

## Slide 20: Bode Plot Examples…
Phase Plot

## Slide 21: Bode Plot Examples…
Phase Plot …

## Slide 22: Bode Plot Examples…
So Complete Bode Plot

## Slide 23: References
Automatic Control System By Hasan Saeed
  Katson Publication

## Slide 24: Questions?

## Slide 25
Thanks