## Slide 1: Control System and Transfer Function
By: Nafees Ahamad,
AP, EECE, Dept.
DIT University, Dehradun

## Slide 2: Open Loop Control System
Faithfulness of an open loop control system depends on the accuracy of the input
Control System
Input
Output
r(t)
c(t)

## Slide 3: Closed Loop Control System (Feedback Control System)
The control action is actuated by an error signal e(t).
A control system without involving human intervention for normal operation is called automatic control system.
Control System
Error
Output
e(t)
c(t)
Feedback System
Input
r(t)

## Slide 4: Transfer Function
Example 1: Determine Vo(s)/Vi(s) of the following circuit.

## Slide 5: Transfer Function …
Laplace Transform
is known as transfer function

## Slide 6: Transfer Function …
Example 2: Determine Vo(s)/Vi(s) of the following circuit.

## Slide 7: Transfer Function …

## Slide 8: Transfer Function
System g(t)
Input
Output
r(t)
c(t)
G
System G(s)
Input
Output
R(s)
C(s)
So, Tranfer function,

## Slide 9: Poles and Zeros
Let a transfer function is given as
Poles: s = 0, -3, -5, -2+j4, -2-j4 (5 poles)
Zeros: s = -2, -4 (2 zeros)
7 is known as gain factor denoted by K.

## Slide 10: Poles and Zeros …
Note:
If poles and zeros are complex, they will be in conjugate
No of poles = No of zeros
In the above example, three zeros are at
Transient behavior depends on poles and zeros
Poles + Zeros + Gain Constant (K) completely define a system (differential equation)
+σ
+jω
0
-3
-5
-2+j4
-2-j4
+j4
-j4
-2
-4
Pole-Zero Diagram

## Slide 11: Thanks